## Slide 1: CyFuzz: A Differential Testing Framework for Cyber-Physical System Development Environments
Shafiul Azam Chowdhury
Dr. Taylor Johnson
Dr. Christoph Csallner
The University of Texas at Arlington
Available: http://shafiulazam.com/cyfuzz
Source Code: https://github.com/verivital/slsf_randgen
VeriVITAL - The Verification and Validation for Intelligent and Trustworthy Autonomy Laboratory
SERC - Software Engineering Research Center
This material is based upon work supported by the National Science Foundation under Grants No. 1117369, 1464311, and 1527398. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.
This material is based upon work supported by the Air Force Office of Scientific Research (AFOSR) contract numbers FA9550-15-1-0258 and FA9550-16-1-0246, and by Air Force Research Lab (AFRL) contract number FA8750-15-1-0105. Any opinions, ndings, and conclusions or recommendations expressed in this publication are those of the authors and do not necessarily reflect the views of AFRL or AFOSR.
6th Workshop on Design, Modeling, and Evaluation of Cyber Physical Systems (CyPhy), Oct. 2016. To appear.
Project Homepage URL

## Slide 2: Engineering process of CPS
Model-based design
Development environments
Simulation & Code Generation
Image on the right: sample Simulink model. This image is licensed under the Creative Commons Attribution-Share Alike 4.0 International license. Media URL: https://commons.wikimedia.org/wiki/File:Simulink_lept.png
Notes: Recently MBD methodology has become the preferred method for designing, modelling and simulating complex dynamic systems [1]

## Slide 3: Defects in Development Environments
Typical assumptions:
Compilers
Code Generators
Simulators
Tools
Do not have bugs
Notes: CC says: You only have full audience attention for the first ca. 5 minutes of your talk. If a speaker does not get to the point on slide 2, people start to zone out and check their email.

## Slide 4: Defects in Development Environments
Typical assumptions:
Compilers
Code Generators
Simulators
Tools
Do not have bugs
MLOC Program
(CPS tool chain)
Without bugs?
Notes: Csmith ref: [7, 8]
CC says: Keep left side, move right side to “Related Work” section at end of presentation

## Slide 5: Defects in Development Environments
Typical assumptions:
Compilers
Code Generators
Simulators
Tools
Do not have bugs
MLOC Program
(CPS tool chain)
Without bugs?
What happens if CPS tool chain injects subtle bugs/security holes into CPS?
Notes: Csmith ref: [7, 8]
CC says: Keep left side, move right side to “Related Work” section at end of presentation

## Slide 6: Tools Improvement Approaches
Formally verifying components
[-] Currently Not feasible
Large codebase
[-] No complete and/or updated specifications
Rapid release cycle of products
Formal
Spec.
Notes: [1, 11]

## Slide 7: Background: Differential Testing
compare
Test Subjects
Code, Model
Compiler 1
Compiler 2
?
Test Generator
generate
compile
Binary 1
Binary 2
execute
Output 1
Output 2

## Slide 8: E.g. Csmith: Yang et al. [2011]
Varying compilers & optimization settings
C
gcc -o1
gcc -o2
llvm -o0
crash
compile
compile
Binary 1
Binary 2
execute
compare
?
Output 1
Output 2
Random Generator
generate

## Slide 9: Background: Differential Testing
compare
Test Subjects
Code, Model
Compiler 1
Compiler 2
?
Random Generator
generate
compile
Binary 1
Binary 2
execute
Output 1
Output 2
[+] Don’t need full formal language specs to find bugs
[+] No false warnings if undefined behaviors are avoided
[+] Inexpensive

## Slide 10: Background: Differential Testing
compare
Test Subjects
Code, Model
Compiler 1
Compiler 2
?
Random Generator
generate
compile
Binary 1
Binary 2
execute
Output 1
Output 2
[+] Don’t need full formal language specs to find bugs
[+] No false warnings if undefined behaviors are avoided
[+] Inexpensive
Others found many bugs with this in production compilers / tools which are part of the CPS tool chain

## Slide 11: New Challenges for Fuzzing CPS tool chain
Having some spec. is useful:
Efficient generator (not generating many invalid tests)
E.g. Csmith generate tests following C99 specification
Image: The C99 standard, screen-captured from URL: http://www.iso.org/iso/iso_catalogue/catalogue_ics/catalogue_detail_ics.htm?csnumber=29237
Notes: Modeling languages are different than Traditional programming languages
modeling language semantics often depend on subtle details, such as two-dimensional layout information, internal model component settings etc.
combination of programming paradigms (e.g., both graphical, data-flow language and textual imperative programming language in the same model

## Slide 12: New Challenges for Fuzzing CPS tool chain
Not the case with Simulink:
Do not have publicly available complete, updated specs.
How to generate valid models which the CPS tool chain can accept without raising errors?
Feedback-driven model generation approach
Guide model generation via CPS tool chain errors/warnings
Notes: [1, 15, 16]
Modeling languages are different than Traditional programming languages
modeling language semantics often depend on subtle details, such as two-dimensional layout information, internal model component settings etc.
combination of programming paradigms (e.g., both graphical, data-flow language and textual imperative programming language in the same model

## Slide 13: New Challenges for Fuzzing CPS tool chain
CPS model contains mix of language paradigms:
Dataflow (nodes, edges) and procedural (C code)
Previous work limited to single paradigm (mostly procedural)
Notes: Modeling languages are different than Traditional programming languages
modeling language semantics often depend on subtle details, such as two-dimensional layout information, internal model component settings etc.
combination of programming paradigms (e.g., both graphical, data-flow language and textual imperative programming language in the same model

## Slide 14: New Challenges for Fuzzing CPS tool chain
Vast search space
Industrial CPS design tools: Very complex modeling languages
Many, many configuration options, platforms, etc.
Notes: Modeling languages are different than Traditional programming languages
modeling language semantics often depend on subtle details, such as two-dimensional layout information, internal model component settings etc.
combination of programming paradigms (e.g., both graphical, data-flow language and textual imperative programming language in the same model

## Slide 15: Our Contributions
Study of publicly available Simulink bug reports
CyFuzz: A conceptual framework for arbitrary CPS environment
Prototype implementation for Matlab’s Simulink
Preliminary evaluation

## Slide 16: A Study of Bugs
Bug reports published for Matlab/Simulink version 2015a on Simulink’s web site Search for: incorrect code generation 17 Feb 2016: 50 bug reports, 47 fixed in subsequent releases
Example finding: Over 50% of reports: Simulation result ≠ Output of generated code  Differential testing seems promising
Our study results online: https://docs.google.com/spreadsheets/d/1l0npmC7k906M5rECmLmfALXT-kLD3mRtX-3ylUXTmxc/pubhtml

## Slide 17: A Study of Bugs
Classification Factor | Bug Reports [%]
Reproducing the bug involves a code generator | 60
Reproducing depends on block parameter values and/or port or function argument values and data-types | 56
Reproducing indicates mismatch between simulation result and generated code's output | 54
Reproducing depends on the way blocks are connected | 36
Reproducing depends on overall model configuration settings | 32

## Slide 18: Review: CPS Models (e.g. Simulink Model)

## Slide 19: Hierarchical Model
1

## Slide 20: CyFuzz: Phases
Random Model Generator
Comparison Framework

## Slide 21: CyFuzz: Phases

## Slide 22: Select Blocks
Generate N blocks N selected randomly from a range Randomly from block libraries, according to customizable weights Currently only from 4 libraries Simulink libraries: 15 built-in plus more from toolboxes Hierarchy up to configurable depth (more on hierarchy later) Customize Csmith to generate C code, integrate via Simulink S-function

## Slide 23: Select Blocks
n: 15
Library | Config. | Actual
Discrete | 35% | 33.33%
Concrete | 35% | 33.33%
Source | 15% | 20.00%
Sink | 15% | 13.33%

## Slide 24: Hierarchical Model Creation
Calls Select Blocks method to create a child (aka sub) model
Child model can select parameters (number of blocks, block selection parameters etc.) on its own
Parent model does not reuse child model (but could)
Child’s own blacklist (and whitelist) of blocks (not all blocks can be used in a child model)

## Slide 25: Configure Blocks
Parameter values currently fixed, but could be random
Configures some (whitelisted) parameters

## Slide 26: Connect Blocks
Maximize number of connected blocks
Randomly choose input/output ports
Prioritize unconnected ports

## Slide 27: Fix Errors
Error in compiling the model

## Slide 28: Fix Errors
Identify problematic components
Exploiting Matlab’s exception handling mechanism

## Slide 29: Fix Errors
Added a new block to fix data-type incompatibility

## Slide 30: Fix Errors
For example:
Algebraic Loop elimination
Model with algebraic loop

## Slide 31: Compile and Simulate
model
Tool chain
configuration
timeout
Compilation is the first step of simulating a model.
simulate will stop immediately if a compilation error occurs.

## Slide 32: Compile and Simulate
ENUM: {success,
Error,
Timed-out}
Logged Signals
Error Messages

## Slide 33: Fix Errors
Simulink error messages are quite detailed Use error message to drive repair action
Our repair may introduce new errors Repeat R times
[+] Easy to implement No knowledge of type rules needed
[+] Worked surprisingly well (in our evaluation)

## Slide 34: Log Signals and Compare
0.5 - 0.4 - 0.1 == 0
False!

## Slide 35: Log Signals and Compare

## Slide 36: Custom Blocks
Integrating procedural code (C/Matlab) in models
Implemented using S-Function interface of Matlab/Simulink

## Slide 37: Custom Blocks (simplified example)
Input
Output
How to calculate output at each simulation step?
static void mdlOutputs(SimStruct *S, ...){
InputRealPtrsType uPtrs =
ssGetInputPortRealSignalPtrs(S,0);
real_T *y =
ssGetOutputPortRealSignal(S,0);
... ??? ...
}
*y = 2.0 *(*uPtrs[0]);

## Slide 38: Custom Blocks
  Csmith-generated functions can not be called safely multiple times after linking as Simulink blocks (re-initialize variables)
  Using data from other blocks in Csmith-generated functions (pass these values to Csmith-generated variables)
  Floating-point support in Csmith is still primitive (detect crash bugs only)
Plugging random C code as Simulink blocks
Harness Csmith to generate random code
High-level Issues:

## Slide 39: Prototype Implementation Details
Comparison Framework:
  Simulink’s Signal Logging API & sim command invocation
  Varies simulation modes
    E.g. “Normal Mode” vs. “Accelerated Mode with Optimization On”

## Slide 40: Research Questions
RQ1. Is the random generator effective? Which portion of the generated models can Simulink simulate?
RQ2. Can CyFuzz find Simulink bugs?
RQ3. What is the runtime of CyFuzz’s phases?
Not included in the evaluation:
Custom Blocks
Hierarchical Models

## Slide 41: RQ1: Effectiveness of Random Generator
[+] Simulink successfully simulated some 80% of generated models
Errors and time-outs fluctuated with library weights

## Slide 42: RQ3: Runtime
Average sum of all phases around 45s
Most expensive phase: Simulation & Signal logging

## Slide 43: RQ3: Runtime
[+] Block Selection Algorithm has O(n) runtime
[+] Scales linearly with number of blocks
  Number of timed-out and error models also increase
  Addressing one type of error in Fix Errors phase reduce number of error models

## Slide 44: RQ2: Effectiveness of Comparison Framework
[+] Independently reproduced a known Simulink bug: Hierarchical model Output differ between Normal and Rapid Accelerator Modes Bug confirmed and fixed in later releases CyFuzz-generated model that triggers the bug:

## Slide 45
X Axes: Simulation Iterations
Y Axes: Block Outputs (numbers)
0 vs. 13E247

## Slide 46: Future Work
Full-fledged fuzzer for Simulink
Incorporate more built-in libraries in the Random Generator
Having custom blocks in generated models (integrate Csmith)
Varying more configuration options in the Comparison Framework
Compare signals in multiple simulation steps
Contribute: https://github.com/verivital/slsf_randgen

## Slide 47: Related Work
Notes: Signal logging in Rapid Accelerator mode: http://www.mathworks.com/help/simulink/ug/exporting-signal-data-using-signal-logging.html#bt0cprf

## Slide 48: Compilers and Type-checker Fuzzers
Jsfunfuzz
LangFuzz [27]
Csmith [10]
Rust Typechecker Fuzzer [11]
Jcrasher [28]
Rugrat [29]
Many core compiler fuzzer [13]
… and many others.

## Slide 49: Testing components of CPS tool chain
Stürmer et al., TSE ‘07 [1]
Code generator testing
Identifies optimizers as most vulnerable
Generates models; needs spec in terms of graph grammar
Uses Reactis (second-order tests)
Sampath et al., RTAS ‘07 [31]
Model preprocessor tester
Requires semantic meta-model of the model preprocessor
Targets Stateflow (Simulink component)
Notes: Sturmer et al cons:
Such specications for code generators might not be available
Whitebox testing in parts is undesirable
Sampath et al cons:
The approach does not scale
The complete specications it needs are not available.

## Slide 50: Testing CPS Models
SimCoTest [17]
Test suite generator for SL/SF controllers
Mohaqeqi et al., TASE ‘16 [32]
Sound test suites for CPS
Conformance testing algorithm
Johnson et al., ICCPS ‘15 [8]
CPS specification mismatch identification
Dynamic analysis approach
Alur et al., CAV ‘09 [33]
Generate symbolic traces
Simulation and static analysis
Coverage improvement

## Slide 51: Thank You!

## Slide 52: References
Notes: Sturmer et al cons:
Such specications for code generators might not be available
Whitebox testing in parts is undesirable
Sampath et al cons:
The approach does not scale
The complete specications it needs are not available.

## Slide 54: Supplementary Materials

## Slide 55: Who uses Simulink/Stateflow?
Aerospace and defence
Airbus, BAE, Bell Helicopter, Boeing, Cessna, EADS, Honeywell, Lockheed Martin, NASA, The US Air Force and Navy
Automotive
Bosch, Daimler, Delphi, Ford, GM, Hyundai, Mazda, Nissan, Toyota, and Volvo
Energy and Industrial Automation
ABB, Alstom, Halliburton, Johnson Controls, and Schlumberger
Biotech and Medical devices
Cochlear, Genetech, Novartis, Pfizer, Philips Healthcare, Roche, and VisionCare
Communications and semiconductors
Alcatel-Lucent, Broadcom, Epson, Fujitsu, Realtek, Renesas, and Vodafone
Notes: CC says: Move at very end (backup section)
Chose SLSF due to its market share as a development tool across CPS industries: Ref: [10]

## Slide 56: SUT Options to Vary
Simulation Modes
  Normal, Accelerated and Rapid Accelerated modes
Compilers
  MinGW/MS Visual C++/GCC
Compiler Optimization
  Various optimization levels/no optimization
Targets and platforms
Simulation solvers
(This is just a list of possibilities, our current setup uses handful of these options listed later)

## Slide 57: Background: CPS model
Parameter: Influences model’s behavior
Block: Node, basic component of CPS model, represents a formula / code Input port: accepts data for block’s processing Connected to a single output port Output port: emits data produced by block Can be connected to multiple input ports Parameter: Influences block’s behavior
Connection: Edge between blocks
Block library: Similar to a standard library of traditional programming language

## Slide 58: Background: CPS model hierarchy
Very popular among industrial Simulink users
Model block: References a group of blocks
Child model: Referenced by a model block
Parent model: Contains a model block

## Slide 59: Background: CPS development tool
Type-checker: Check if CPS model is syntactically well-formed E.g.: Data type mismatch between connected output and input ports
Simulator: Numerically solve model’s formulas Calculate blocks’ outputs For N simulation steps Mode: Interpreted vs. Compiled vs. Combinations Simulink: “Accelerator”, “Rapid Accelerator”, etc.
Signal: Output of a block's port at a particular simulation step
Code generator: Generate native code for (embedded) target platform